# Text boxes

IVG-HP200S-AE

2.0M H.265 Intelligent analysis IP Module

Features:

- 2.0M HD resolution,clear and fine images;

- Support multiple intelligent analysis;

- Support 2D/3D noise reduction,digital wide dynamic;

- Advanced H.265/H.264 video compression,Super low rate,high definition quality of image;

- Professional anti-lightning,conform to GB/T17626.5 and IEC61000-4-5。

- Support ONVIF ,access third party；

- Support various mobile monitoring(iPhone,Android);

- Provide web、CMS、center platform management software MYEYE,provide SDK development；

- Support cloud technology,easy to achieve network penetration,fro in-line and alarm information pushed；

Parametes：

| Model | IVG-HP200S-AE |
| --- | --- |
| System structure | Embedded RTOS, dual-core 32-bit DSP (Hi3516CV300),pure hard compression ,watch dog |
| Sensor | 2.0M 1/2.7 " SC2235 CMOS sensor,color 0.1Lux@F1.2,black/white 0.01Lux@F1.2 |
| Video compression | H.265/H.264 support dual stream,AVI;0.1M~8Mpbs variable;1~30f/s variable |
| Image output | Main stream: 1920*1080@25fps,1280*720@25fps; sub-stream: 704*576@25fps; |
| Shutter | 1/50(1/60)s to 1/10,000s |
| Lens | No |
| Day and night | Support IR-CUT |
| Noise reduction | Support 2D/3D |
| Wide dynamic | Support |
| Auto iris | N/A |
| Audio compression | G.711 standard compression,support two-way Bidrectional Talk,support for audio and video synchronization |
| Audio interface | 1ch input,level:2Vp-p,impedance:1kΩ,support sound pick-up input;1ch output,impedance:16Ω,30mw,support microphone; |
| Network interface | 1*RJ45 10/100M adaptive Ethernet port;support RTSP/FTP/PPPOE/DHCP/DDNS/NTP/UPnP etc |
| Extension interface | 1*USB,support WIFI/3G,support SD；1ch Alarm output；reset key；1ch Alarm input or LED panel；RTC battery |
| Singal interface | One photo resistance interface,one IR-CUT interface ,support photo resistance signal and IR-CUT links to IR |
| PTZ | N/A |
| Motor interface | N/A |
| Alarm I/O | 1/0(support alarm input and video link to background) |
| WIFI interface | N/A |
| Reset interface | N/A |
| SD Card | N/A |
| Reliability | Comprehensive lightning protection, 7 * 24 hours 65 ℃ high temperature stable and reliable testing |
| Intelligence analysis | Alarm line,alarm region,goods stranded,video block,fuzzy detection,scene change |
| Other function | Support WEB,OSD,live video transmission,motion detect and IO alarm,front-end storage/playback/download, and center reminder and image linkage,support JPEG capture；united remote client monitoring sofaware、MYEYE;perfect SDK; |
| ONVIF | Support |
| Mobile monitoring | Support multiple mobile monitoring（iOS，Android） |
| Power | DC12V/2A input, power consumption:≤3W |
| Dimension | 38mm*38mm |
| Other | Does not accept any custom. |